## Slide 1: Applying Reinforcement Learning to Maximise PV Self-Consumption for Electric Vehicle Charging
Author: Eric Massip Cano
Promotor: Prof. dr. ir. Geert Deconinck
Assesor: Dr. ing. Ján Drgona
Supervisors: Dipl. ing. Brida Verwiyni Mbuwir & Dr. ing. Klaas Thoelen

## Slide 2: Index
ESAT
Conclusion
Introduction
Data Analysis
Demand Response Algorithm
Experiment setup
Results

## Slide 3: Introduction: EV Charging
ESAT
    No green-house gas emissions
    High electricity demand
        Solution RES Self-Consumption

## Slide 4: Introduction: PV Installation at
ESAT
4 orientations facing North, South, East and West
24 three-phase inverters
Maximum generation capacity 450 kW
G. H. Yordanov, F. Smolders, A. Olaerts, G. Verbeek, K. Baert, and J. Driesen. A 368-kWp Grid-connected PV System : Known and Hidden Losses. EU PVSEC Programme Planner, pages 1909–1914, 2017.

## Slide 5: Introduction: EV Charging Infrastructure at
ESAT
Charging Station | Connectors | Charging Rate | Quantity
Simple | 1 |  | 6
Smart | 2 |  | 6
Supercharger | 1 |  | 1

## Slide 6: Introduction: Smart Charging
ESAT
Demand Response Algorithms: Control algorithms that, given information about the environment, either delay or proceed with the charging in order to optimize the charging for a given goal.

## Slide 7: Introduction: Our Goal
ESAT
Balance the aggregate load of charging EVs against the PV energy generated by the PV installation, by means of a DR algorithm using Reinforcement Learning.

## Slide 8: Index
ESAT
Conclusion
Introduction
Data Analysis
Demand Response Algorithm
Experiment setup
Results

## Slide 9: Data Analysis: PV Dataset
ESAT
Average charging rate = 7.5 kWh
Nº of charging connectors available = 8
Maximum power demand in an hour = 60 kW
Scaling factor = 20 %

## Slide 10: Data Analysis: Charging Transactions Dataset
ESAT
Arrival times distribution:
  Mean = 08:05h
  IQR = [06:41h, 07:52h]
Departure times distribution:
  Mean = 14:41h
  IQR = [14:15h, 16:00h]
EV Charging Behaviour

## Slide 11: Data Analysis: Charging Transactions Dataset
ESAT
Sojourn times distribution:
  Mean = 8.3 hours
  IQR = [5.3-8.9] hours
Charging times distribution:
  Mean = 2.62h
  IQR = [1.9, 3.1] hours
EV Charging Behaviour

## Slide 12: Data Analysis: Charging Transactions Dataset
ESAT
Idle times distribution:
  Mean = 5.2 hours
  IQR = [3.8, 6.5] hours
EV Charging Behaviour

## Slide 13: Index
ESAT
Conclusion
Introduction
Data Analysis
Demand Response Algorithm
Experiment setup
Results

## Slide 14: Demand Response Algorithm: Markov Decision Process
ESAT
State space
where
= timeslot
= forecast PV generated at timeslot
= aggregate state space
Action space
= Set of possible actions at state s
N. Sadeghianpourhamami, J. Deleu, and C. Develder. Definition and evaluation of model-free coordination of electrical vehicle charging with reinforcement learning. sep 2018

## Slide 15: Demand Response Algorithm: Markov Decision Process
ESAT
Cost Function
Cost Demand
Cost Penalty
Cost Demand = Load balancing between production and consumption
Cost Penalty = Penalty for cars that leave before being fully charged
+

## Slide 16: Demand Response Algorithm: Sampling Trajectories
ESAT
N. Sadeghianpourhamami, J. Deleu, and C. Develder. Definition and evaluation of model-free coordination of electrical vehicle charging with reinforcement learning. sep 2018

## Slide 17: Demand Response Algorithm: Action-Value Function
ESAT
In RL, an agent takes actions to move from state s to s’ based on a learned policy.
Every state-action pair has an associated cost = Q-value
The goal is to find the optimal policy in order to minimize the expected accumulated cost.
The Q-values of the learned policy are iteratively updated using the Bellman equation:

## Slide 18: Demand Response Algorithm: Batch RL Algorithms
ESAT
Fitted Q-Iteration
Fitted Q-Iteration Reverse
However, the amount of possible state-action pairs is too large.
The action-value function needs to be approximated using a batch RL algorithm.

## Slide 19: Index
ESAT
Conclusion
Introduction
Data Analysis
Demand Response Algorithm
Experiment setup
Results

## Slide 20: Experiment Setup: Data Preparation
ESAT
Charging Transactions dataset
PV dataset
Transactions from Aug 8th to May 3rd 2019
Training set = 76 days
Test set = 19 days
Episodic days from 6am to 10pm (16 hours)
Duration of a time slot = 2 hours
= 8 timeslots
PV power generated every 15min during the 97 days of the dataset
From 00:00h to 23:45h

## Slide 21: Experiment Setup: Function Approximator
ESAT
Baseline network
PV network

## Slide 22: Index
ESAT
Conclusion
Introduction
Data Analysis
Demand Response Algorithm
Experiment setup
Results

## Slide 23: Results: BAU vs FQI vs FQIR
ESAT
Normalized cost relative to the optimum policy
Percentage of PV energy consumed

## Slide 24: Results: Morning Charging FQIR
ESAT

## Slide 25: Results: Morning Charging FQI
ESAT

## Slide 26: Results: Morning Charging
ESAT
% PV consumed = 10 %
% PV consumed = 100 %
% PV consumed = 100 %
Behaviour: Two cars connected early in the morning

## Slide 27: Results: Late Charging
ESAT
% PV consumed = 80 %
% PV consumed = 100 %
% PV consumed = 80 %
Behaviour: One car connected early in the morning with a late departure, and another one connected in the afternoon

## Slide 28: Results: Cloudy Day
ESAT
% PV consumed = 10 %
% PV consumed = 10 %
% PV consumed = 20 %
Behaviour: Two cars connected early in the morning, and three more connected during the rest of the morning

## Slide 29: Index
ESAT
Conclusion
Introduction
Data Analysis
Demand Response Algorithm
Experiment setup
Results

## Slide 30: Conclusion
ESAT
69.4 % of the total energy consumed following the best policy learned via the proposed approach is PV self-consumed, improving by 37.6 % over the BAU and below the optimal policy by just 1.2 %.
The strategy of the FQI algorithm is very simplistic but effective if there are no cars with late departures.
The FQIR algorithm doesn’t wait, tries to charge when there is enough forecast PV energy.
The proposed approach is proved to be scalable.

## Slide 31: Future Work
ESAT
Test the performance of the proposed approach on a more complex dataset with more stochasticity and more charging stations
Investigate the effect of lower time steps
Introduce a new term in the cost function to encourage the charging to happen as soon as there is enough PV energy generated available for charging
Re-design the state space adding a 3rd dimension to include information about the charging rate for every connected car. Experiment with Convolutional Neural Networks.
Change or combine the objective function for other applications (load flattening, electricity price reduction)

## Slide 32: Thank you!
ESAT

## Slide 33: Appendix
ESAT

## Slide 34: Data Analysis: Charging Transactions Preprocessing
ESAT
C. Develder, N. Sadeghianpourhamami, M. Strobbe, and N. Refa. Quantifying flexibility in EV charging as DR potential: Analysis of two real-world data sets. In 2016 (SmartGridComm), pages 600–605. IEEE, nov 2016.

## Slide 35: Data Analysis: Charging Transactions Preprocessing
ESAT
Completed Transaction
Non-completed Transaction

## Slide 36: Data Analysis: EV Charging Behaviour
ESAT

## Slide 37: Data Analysis: Conclusions
ESAT
Is EnergyVille a charge near work cluster? Yes!
Arrival times: Early morning (around 6-9am).
Departure times: Late afternoon.
Sojourn times: Average around 9 hours. Min-Max = [5.00, 18.52].
Charging times: It normally happens throughout the day, car sleepovers are an exception.
Idle times: Average is 5h 30min. Min-Max = [0, 15.54].
Is it possible to predict the state of charge only with information about the charging power? No, alternatives:
  Ask the user
  Extract it directly from the car
C. Develder, N. Sadeghianpourhamami, M. Strobbe, and N. Refa. Quantifying flexibility in EV charging as DR potential: Analysis of two real-world data sets. In 2016 (SmartGridComm), pages 600–605. IEEE, nov 2016.

## Slide 38: Experiment Setup: Performance Evaluation
ESAT
Normalized cost relative to the optimum policy

## Slide 39: Results: Parameter Selection
ESAT
Increasing Cost Penalty
Scaling up
Adding Forecast PV Information
Training with more sampling trajectories

## Slide 40: Results: Late Charging FQIR
ESAT

## Slide 41: Results: Late Charging FQI
ESAT

## Slide 42: Results: Cloudy Day FQIR
ESAT

## Slide 43: Results: Cloudy Day FQI
ESAT